Various production methods with FORMETAL Ypsilon compared to previous methods

| Calculation example: Production of a model for one figure approx. 7.0 m high with 2.0 m diameter | Previous production method with styropor and plaster | Production with FORMETAL Ypsilon and glasfibre |
| --- | --- | --- |
| Costs for material | 1,000.00 EUR | 2,500.00 EUR |
| Costs for cleaning, etc. | 500.00 EUR |  |
| Costs for disposing of material | 1,000.00 EUR | 500.00 EUR |
| Labour costs | 25,000.00 EUR | 15,000.00 EUR |
| Total costs | 27,500.00 EUR | 18,000.00 EUR |
| Explanation regarding labour costs: | Assuming the production would take approx. 20 days with 4 workers = 640 hours at EUR 40,00 / hour | Using Formetal allows a reduction to only 13 days with 4 workers = 416 hours at EUR 40,00 / hour |
| Explanation regarding production method: | The figure is put together with large pieces of foaming material and roughly cut into form. Then this form is coated with plaster and surfaced to achieve the final form | The basic construction is made of welded steel. It is also possible (but not necessary) to apply a wooden construction on top and then nail FORMETAL onto it. FORMETAL can then be coated with glasfibre. |
| Aspects for using Formetal: |  |  |
| Labour/Labour costs | Very high | Extremely lower |
| Machines needed | Extra machines/tools necessary | Hardly any extra machines needed |
| Room needed | Extra space/room needed | No extra room needed |
| Contamination | Very high | Almost no contamination |
| Noise during manufacture | High | Low |
| Health | Injurious to health | Glasfibre resin can steam out |
| Protective clothing | Absolutely necessary | Only necessary in certain cases |
| Pollution | Pollution of the environment | Only the resin can cause pollution |
| Loss of material | Very high (up to 50%) | Almost no loss of material |
| Weight of the model | Heavy | Light |
| Use as end product | Almost not possible | Very well possible |
| Use for outside areas | Not possible | Very well possible |
| Expert knowledge for manufacturing | Knowledge as modeller necessary | Knowledge as welder necessary |
| Disposal of material | Expensive, because whole model has to be disposed of | Only the glasfibre has to be disposed of (if not needed) |
| Repairs + Changing of the model | Very labour-intensive because form has to be re-plastered | Very easy, because form only needs to be pressed into another form |
| Participation of the customer | Hardly possible | Possible from the very beginning |
| Cost for the end product | In addition very high | Model may be used as the end product |
| Further explanations: | The common production method certainly has the advantage that the companies do not have to change their working process. Though, regarding globalisation every company is seeking to work more cost efficiently, in order to master competition. The enormous amount of contamination and the security measures taken for the workers are a serious problem. Especially when looking toward the important issue of pollution control. | Reorganisation regarding the production method will be necessary. Due to the enormous amount of time saving it will become possible to work a lot more cost efficient. This will entail additional orders and a big step ahead in competition. FORMETAL can be recycled without any additional costs. The steel base can be used again for other projects. The fact that the customer can participate in the project at a very early stage will save a lot of time and money and simplifies the order extremely. |